## Slide 1
M.Tech/MCA Program
Advanced Industry Integrated Programs
Jointly offered by University and LTIMindTree
Review III
QualitySentinel AI
Multimodal Construction Quality Investigation & Prevention Platform
Rushikesh Nirmal
25MML0016 · M.Tech AI & ML, VIT Vellore
Knowledge partner | Implementation partner
Notes: QualitySentinel AI takes a construction site photograph through to a probable cause and a ranked set of preventive actions for the next pour.

## Slide 2
A site photo finds the crack. Nobody finds why — so the same defect returns.
Introduction
QualitySentinel AI
Where inspection stops today
What QualitySentinel AI adds
What happened?
Defect located on the site photo
DETECTION
How serious?
Risk scored from the pour record
RISK ASSESSMENT
Why?
Probable cause from three specialists
INVESTIGATION
How to prevent it?
Fixes ranked for the next pour
PREVENTION
Built on public defect imagery and a pour-record dataset generated from documented concrete behaviour.
Notes: Detection is where inspection stops today. The project adds the next three questions: how serious, why, and how to prevent it.

## Slide 3
From site photograph to preventive action — every number computed, never generated.
Objective
QualitySentinel AI
Detect
Five defect classes located on a site photo
1
Score
Risk level, with the factors that drove it
2
Investigate
Specialist agents, each on its own evidence
3
Prevent
Fixes ranked by the risk each one removes
4
Deliver
One dashboard that shows its own uncertainty
5
Notes: Five objectives, one per stage. The rule throughout: models compute every number, language models only reason over that evidence.

## Slide 4
Clean, audited data before any model sees it
Three Roboflow sources merged and remapped to five classes
Audit dropped a greyscale class (Rust) and near-full-frame boxes
4,000 pour records generated from Abrams' law and IS 456, seeded
Module 1 — Data Acquisition & Preparation
QualitySentinel AI
9,278
site images
21,685
labelled defect boxes
5
defect classes
4,000
pour records
Notes: Three public Roboflow datasets were merged and audited before training. The audit removed a greyscale class and near-full-frame boxes. Pour records are synthetic, generated from Abrams' law and IS 456, because linked supplier data is not public.

## Slide 5
What is wrong, and where
YOLOv8 locates five defect classes on a site photo
The most severe defect, and its area, feeds the risk model
Pipeline validated on a 300-image run (mAP@50 0.438); full GPU training is the open item
Module 2 — Construction Defect Detection
QualitySentinel AI
Severity order — the worst defect drives risk
Rebar exposed reinforcement
1
Spalling concrete broken away
2
Crack surface or through crack
3
Scaling surface flaking
4
Efflorescence salt deposits on the surface
5
Notes: YOLOv8 finds five defect classes. The most severe defect found is passed to the risk model. Current weights are a 300-image validation run; full GPU training is the open item.

## Slide 6
Severity, and the reasons behind it
XGBoost scores the pour record as Low, Medium or High
Exact TreeSHAP explains every score, always toward High
Blank fields are scored at the median but shown as ‘not recorded’
Module 3 — Quality Risk Assessment
QualitySentinel AI
74.5% held-out accuracy · baseline 44.4%
What drove a High score — SHAP contribution
Chart: 
| Curing 2 days | 28-day strength 17 MPa | Cover 18 mm | Crack width 2.4 mm | Defect: Rebar
value | 2.3 | 1.48 | 1.26 | 1.11 | 0.66
Notes: XGBoost reaches 74.5% against a 44.4% majority baseline. TreeSHAP explains each score toward the High class, so the sign never flips. A blank field is shown as not recorded, never as a measured value.

## Slide 7
Three slices of evidence, one chair
Three specialists run in parallel, each blind to the others’ evidence
Evidence is supplied, never recalled: IS 456 values and retrieved statistics
‘Insufficient evidence’ is a valid verdict — no data, no blame
Module 4 — Multi-Agent Root-Cause Investigation
QualitySentinel AI
Pour record
+ defect
Materials
mix · supply · cover
Site execution
curing · heat · age
History
matched past pours
Chair
probable cause · gaps
Notes: Three specialists each see only their own slice of the evidence and run in parallel. They are given IS 456 values and retrieved statistics instead of recalling them. A chair weighs their findings.

## Slide 8
Fixes ranked by the risk each one removes
Every off-target field becomes a fix with its IS 456 basis and owner
The risk model re-scores the pour with the fixes applied
Shapley values share the credit — alone, each fix reads near zero
Module 5 — Preventive Action
QualitySentinel AI
High → Medium all six fixes
Share of the risk removed
Chart: 
| Curing duration | 28-day strength | Cover depth | Water-cement ratio | Pour temperature | Slump
value | 0.49 | 0.24 | 0.15 | 0.07 | 0.05 | 0.01
Notes: Every off-target field becomes a candidate fix. The risk model re-scores the pour with fixes applied, and Shapley values share the reduction fairly, because one fix alone barely moves a pour failing on several fronts.

## Slide 9
One photograph in, every stage on one screen
FastAPI serves /detect, /assess, /prevent and /investigate
React dashboard fills each panel as its stage finishes
Detection, risk and fixes in about a second; agents in about five
Module 6 — Dashboard & Deployment
QualitySentinel AI
Live run on the demo pour — risk on the left, ranked fixes on the right
Notes: FastAPI serves four endpoints; the React dashboard fills each panel as its stage finishes. The screenshot is a live run on the demo pour.

## Slide 10
Inspection stops at detection — cause and prevention are left to memory.
Problem Statement
QualitySentinel AI
Today
Photo logged, record closed
Mix, curing and cube tests in separate systems
Cause decided from recollection
Same defect on the next pour
Needed
One record across photo and pour data
A probable cause backed by evidence
Fixes ranked by the risk they remove
Honest about what was not measured
Notes: Defect records close at detection. Mix, curing and test data live in separate systems, so the cause is decided from memory and the same defect returns.

## Slide 11
Models compute every number; language models only reason over the evidence.
Methodology
QualitySentinel AI
Site photo
+ pour record
Detect
YOLOv8
Score
XGBoost + SHAP
Prevent
counterfactual + Shapley
Investigate
3 specialists + chair
Dashboard
FastAPI + React
Imagery 3 public datasets, CC BY 4.0
Pour records synthetic, from Abrams' law and IS 456
Schema real fields — site data drops in unchanged
Notes: Detection, then risk scoring, then prevention and investigation in parallel, then the dashboard. Imagery is public; pour records are synthetic but use the real schema.

## Slide 12
Each layer uses the simplest method whose output can be checked.
Approach / Algorithms / Tools
QualitySentinel AI
Detection
YOLOv8 object detection
Ultralytics · OpenCV · Pillow
Risk scoring
Gradient-boosted trees + exact TreeSHAP
XGBoost · scikit-learn · joblib
Prevention
Counterfactual re-scoring + Shapley values
Python on the trained risk model
Investigation
Parallel specialist agents + a chair
gpt-oss-120b on Groq · JSON output
Service
Typed REST API
FastAPI · Pydantic · Uvicorn
Dashboard
Progressive single-page app
React · Vite · hand-built SVG charts
Notes: Each layer uses the simplest method whose output can be checked: an object detector, gradient-boosted trees with exact SHAP, Shapley attribution, and agents constrained to JSON.

## Slide 13
Each specialist blamed its own slice only when that slice was at fault.
Findings and Results
QualitySentinel AI
74.5%
risk accuracy · baseline 44.4%
3 / 3
separation cases passed
0.20
confidence on a compliant pour
Case | Materials | Site execution | History | Chair
Bad mix, good site | Primary 0.95 | Not a factor | Contributing | Cover depth · 0.92
Good mix, bad site | Not a factor 0.95 | Primary 0.95 | Primary | Curing · 0.88
All within spec | Not a factor | Not a factor | Not a factor | No cause · 0.20
Notes: The separation test uses three constructed cases with known answers. Each specialist claimed the cause only when its own slice was at fault, and on a compliant pour the chair returned no cause at 0.20.

## Slide 14
Testing exposed four failures — each one fixed, not hidden.
Findings and Results
QualitySentinel AI
Invented code limits
Found Agent cited 20 mm column cover; IS 456 says 40 mm
Fixed IS 456 values supplied; only those may be cited
Language-model wording drift
Found Wrong site methods — ‘add sand’ to cut slump
Fixed Fixed templates; the model removed from Module 5
Evidence leak between agents
Found Shared factor list let Materials see curing days
Fixed Per-slice factors; Materials now stands down
Guesses shown as measurements
Found Blank fields shown at their dataset median
Fixed Marked ‘not recorded’; never used as evidence
Notes: Testing found four failures, and each fix is part of the result: invented code limits, language-model wording drift, an evidence leak between agents, and guesses shown as measurements.

## Slide 15
All six modules run end to end from one site photograph.
Conclusion
QualitySentinel AI
Delivered
Photo → risk → cause → fixes on one screen
Every number computed by a model, not generated
Missing data stated, never guessed
Limitations
Pour records are synthetic
Detector trained on a 300-image run
Fields treated as independent in the counterfactual
Next steps
Full-dataset GPU training of the detector
Crack size from the crack, not its box
Persist inspections; verify the IS 456 table
Containerise for deployment
Notes: All six modules run end to end. The main limitations are synthetic pour data and the subset-trained detector; the next steps follow directly from them.

## Slide 16
Thank you to everyone who made this project possible.
Acknowledgement
QualitySentinel AI
VIT Vellore & LTIMindtree
for the Advanced Industry Integrated Program that made this project possible
Faculty guide & industry mentor
for guidance, honest feedback and reviews at every stage
L&T EduTech & open source
for programme support, and the public datasets and tools this work builds on
Notes: Thanks to the program partners, my guide and mentor, and the open-source and dataset authors.

## Slide 17
[1] G. Jocher, A. Chaurasia, J. Qiu, “Ultralytics YOLOv8,” 2023. github.com/ultralytics/ultralytics
[2] T. Chen, C. Guestrin, “XGBoost: A Scalable Tree Boosting System,” Proc. ACM SIGKDD, pp. 785–794, 2016.
[3] S. M. Lundberg, S.-I. Lee, “A Unified Approach to Interpreting Model Predictions,” NeurIPS, 2017.
[4] S. M. Lundberg et al., “From local explanations to global understanding with explainable AI for trees,” Nature Machine Intelligence, 2, pp. 56–67, 2020.
[5] L. S. Shapley, “A Value for n-Person Games,” Contributions to the Theory of Games II, Princeton Univ. Press, pp. 307–317, 1953.
[6] P. Lewis et al., “Retrieval-Augmented Generation for Knowledge-Intensive NLP Tasks,” NeurIPS, 2020.
[7] OpenAI, “gpt-oss-120b & gpt-oss-20b Model Card,” 2025.
[8] Bureau of Indian Standards, IS 456:2000 — Plain and Reinforced Concrete, Code of Practice (Fourth Revision).
[9] D. A. Abrams, “Design of Concrete Mixtures,” Bulletin 1, Structural Materials Research Laboratory, Lewis Institute, 1918.
[10] Chow et al., Automation in Construction, 2021 — construction defect detection.
[11] Wang & El-Gohary, Automation in Construction, 2024 — construction-site visual compliance.
[12] Roboflow Universe — public concrete crack, spalling and defect datasets, CC BY 4.0.
References
QualitySentinel AI
Notes: Key references for the methods used.