## Slide 1
M.Tech/MCA Program
Advanced Industry Integrated Programs
Jointly offered by University and LTIMindTree
Review II
QualitySentinel AI
Multimodal Construction Quality Investigation & Prevention Platform
Rushikesh Rahul Nirmal
25MML0016 · M.Tech Artificial Intelligence & Machine Learning
VIT Vellore · Jointly offered with LTIMindtree
Knowledge partner | Implementation partner

## Slide 2
A site engineer photographs a crack, logs it, and the record closes. Detection is where construction quality inspection stops.
Nobody systematically establishes why the defect appeared. The curing log, the batch ticket and the cube test sit in separate systems and are never read together.
So the same failure recurs on the next pour. The knowledge stays in individual engineers' heads rather than in the process.
Rework is costed at 5–10% of project value, and most of it is a repeat of something already seen elsewhere on the same site.
Existing tools detect defects on one screen and hold material records on another, but nothing reasons across them — which is where the preventable repetition lives.
The gap this project addresses: taking a photograph through to a defensible cause and a corrective action for the next pour, not just a bounding box.
Introduction
QualitySentinel AI

## Slide 3
Detect and classify surface defects from an ordinary site photograph across five classes, with per-finding confidence an engineer can act on.
Score quality risk from the pour record — mix, curing, cover and test results — and expose the factors that drove the score rather than a bare number.
Investigate probable cause with specialist agents that each see only their own evidence, so their verdicts cannot simply agree with one another.
Ground the investigation in retrieved statistics from past records, so a claimed pattern is a measured one.
Deliver it as a working inspection dashboard, and state the system's own uncertainty on every panel rather than hiding it.
Scope: a complete working platform on public defect imagery and a synthetic pour dataset built from IS 456 relationships, not a component study.
Objective
QualitySentinel AI

## Slide 4
Modules 1 and 2 · what is wrong, and where
Three public Roboflow datasets merged into one 5-class set — 9,278 images and 21,685 boxes across Crack, Spalling, Rebar, Efflorescence and Scaling.
Audit before training caught three faults: a source with unlabelled class names, 932 near-full-frame boxes that teach nothing about location, and one source entirely greyscale.
Rust was dropped on that last finding. It is defined by being orange-brown, so 2,217 greyscale training boxes would have taught the model to fire on shadows.
YOLOv8 detector served through FastAPI; the most severe defect found is passed forward as the input to risk scoring.
Current weights are a 300-image validation run at mAP@50 0.438. Full-dataset GPU training is the outstanding item before the final review.
Modules 1 & 2 — Data Pipeline and Defect Detection
QualitySentinel AI

## Slide 5
Module 3 · severity, and the reasons behind it
XGBoost over 4,000 synthetic pour records — supplier, grade, water-cement ratio, curing days, ambient temperature, cover depth, 28-day cube strength and the observed defect.
Held-out accuracy 74.5% against a 44.4% majority-class baseline, a 30.1-point lift. Low and High are almost never confused; error concentrates on the Medium boundary, where it belongs.
Per-prediction attribution from exact TreeSHAP, computed through the booster so the explanation is the model's own, not a surrogate.
Contributions are always taken toward the High class, giving one consistent risk axis — otherwise the sign of an explanation flips with the verdict.
Recovered drivers rank as curing duration, 28-day strength, cover depth, crack width — the four things a site engineer checks, found without being told.
A missing field falls back to the training median rather than zero — read as zero, an unrecorded curing log would score High on a pour nobody measured.
Module 3 — Quality Risk Assessment
QualitySentinel AI

## Slide 6
Module 4 · the core contribution of this project
Three specialist agents examine strictly non-overlapping evidence in parallel — mix and supply, site execution, historical record — then a fourth weighs their findings.
The history specialist is handed retrieved statistics rather than asked to recall a pattern: curing under three days shows 62% High risk against a 19% base rate across 376 matched records.
Every agent returns structured JSON with an explicit insufficient_evidence verdict, so declining to blame anything is a first-class answer rather than a failure.
Separation validated on three constructed cases with known answers. Each specialist claimed primacy only when its own slice was at fault and stood down when it was clean.
On a compliant pour all three declined and the chair returned no identifiable cause at 0.20 confidence — the failure mode this architecture exists to prevent. Served by openai/gpt-oss-120b via Groq: four agents, about 3,900 tokens, under five seconds.
Module 4 — Multi-Agent Root-Cause Investigation
QualitySentinel AI

## Slide 7
Imagery
Three public datasets merged with class renumbering, a near-full-frame box filter and a cap on the dominant class. Audited for label geometry and colour-space consistency before any training.
Synthetic pour records
Four thousand records generated from documented concrete relationships — Abrams' law for water-cement ratio against strength, IS 456 curing durations extended in hot weather, nominal cover by element, corrosion risk rising with age where cover is short.
Eight interacting terms with noise, overlapping supplier quality and 5% label disagreement, tuned so roughly 78% accuracy is achievable. A generator yielding 99% would mean the model was reciting the rules rather than learning them.
The model observes only measurable fields. It never sees the latent risk function.
Agent contract
Deterministic models compute every number → agents reason over that evidence → no measurement in the system originates from a language model.
Methodology / Modelling Plan
QualitySentinel AI

## Slide 8
Merged image set of 9,278 across train, validation and test, carrying 21,685 boxes. Class share runs 48% Crack down to 2.6% Scaling — reported per class, never as a single mAP that would hide it.
Box geometry audited before training: Efflorescence 20.7% and Crack 16.0% of boxes exceeded half the frame. Filtering on area alone was rejected — a diagonal crack legitimately spans the frame — so the filter removes boxes wide and tall.
Colour-space check across sources: 40 of 40 sampled images from one dataset were greyscale against 1 of 40 and 6 of 40 in the others. This is what disqualified Rust.
Pour records split 45/36/19 across Low, Medium and High. All generation is seeded, so a rebuild reproduces the same dataset and the same model scores.
Data provenance — stated explicitly
Defect imagery is public and CC BY 4.0. The pour records are synthetic: linked defect-to-supplier data is not publicly available and company data cannot be used in an academic project. The schema is the real one, so field records replace the synthetic layer without a code change.
Data Preprocessing & EDA
QualitySentinel AI

## Slide 9
Detection
Ultralytics YOLOv8 · five defect classes · OpenCV and Pillow for the label audit and merge pipeline
Risk and explanation
XGBoost gradient-boosted trees · exact TreeSHAP through the booster · scikit-learn for splitting and metrics · joblib for model persistence
Agents
openai/gpt-oss-120b served by Groq · three specialists run concurrently on a thread pool, then a synthesis chair · JSON-constrained responses with a tolerant parser and rate-limit backoff
Data and service
NumPy · pandas · FastAPI · Pydantic · Uvicorn · python-dotenv for credential handling
Dashboard
React with Vite · hand-built SVG overlay for detection boxes and a diverging SHAP factor chart · no charting library, nothing loaded from a CDN
Verification
Constructed-case evaluation for agent separation · majority-class baselines reported beside every accuracy figure · colour-blind separation of the chart palette computed, not eyeballed
Approach, Algorithms & Tools
QualitySentinel AI

## Slide 10
Completed for Review II
Dataset merge and audit — three sources to five classes, with the greyscale and box-geometry findings acted on
Synthetic pour generator built from IS 456 relationships, deliberately noisy and seeded for reproducibility
Risk model at 74.5% against a 44.4% baseline, with TreeSHAP attribution served per prediction
Four-agent investigation with retrieval-grounded history, validated on constructed cases
FastAPI backend and React inspection dashboard — detection, risk and investigation all live
Planned before final review
Full-dataset GPU training of the detector, replacing the 300-image validation weights
Ground the agents' code citations — an agent was found citing 20 mm minimum cover for a column where IS 456 requires 40 mm
Module 5 — preventive action ranked by expected effect, generated from the risk factors and the panel conclusion
Persist inspections so the history specialist reasons over this project's own record rather than the synthetic set
Project Plan & Milestone Progress
QualitySentinel AI

## Slide 11
Pipeline Structure
QualitySentinel AI
OFFLINE · build and train
Dataset merge
9,278 images · 5 classes
Label audit
greyscale · box geometry
YOLOv8 detector
mAP 0.438 · GPU run pending
XGBoost + TreeSHAP
74.5% vs 44.4% baseline
LIVE · on a site photograph
Detection
defects located and ranked
Risk assessment
severity · driving factors
Three specialists
mix · execution · history
Panel chair
probable cause · evidence gaps
under a second
about five seconds
Separation test · three constructed cases with known answers, each specialist standing down when its own evidence is clean
verdicts tracked the evidence, confirming the separation is functional rather than cosmetic
Deterministic models compute every number; the agents reason over that evidence and never originate a measurement.